## Slide 1
DEPT. OF ENVIRONMENTAL ENGINEERING
01
Removing Microplastics with Sand-Biofilm Filters
A low-cost filtration design for small coastal treatment plants — thesis defense, Noura Al-Harbi.
MSc DEFENSE · 2026
Notes: Introduce yourself, program, supervisors. One sentence on why this matters locally.

## Slide 2
OUTLINE
DEPT. OF ENVIRONMENTAL ENGINEERING
02
Defense roadmap
1
Background & research gap
2
Research questions
3
Methodology
4
Results & discussion
5
Conclusions
Notes: Roadmap reduces panel cognitive load. Mention backup slides exist for detail questions.

## Slide 3
BACKGROUND
DEPT. OF ENVIRONMENTAL ENGINEERING
03
Coastal plants discharge microplastics untreated
Secondary treatment misses small particles
Particles under 300 micrometers pass conventional clarifiers largely intact.
Membrane upgrades are unaffordable locally
Capex and energy costs exceed small-plant budgets by 4-6x.
Biofilm-sand hybrids are understudied
No published data for Red Sea salinity and temperature ranges.
300µm
Particle size below which conventional treatment stops working.
Notes: Establish the gap: effective + affordable + local conditions. Cite sources verbally.

## Slide 4
RESEARCH QUESTIONS
DEPT. OF ENVIRONMENTAL ENGINEERING
04
Three questions this thesis answers
1
Removal efficiency?
Can sand-biofilm reach 90% removal below 300µm?
2
Salinity effect?
Does Red Sea salinity degrade biofilm performance?
3
Operating cost?
Can OPEX stay under $0.05 per cubic meter?
Notes: Panels grade conclusions against these exact questions. Pause here.

## Slide 5
METHODOLOGY
DEPT. OF ENVIRONMENTAL ENGINEERING
05
Pilot rig ran 112 days across three salinities
STEP 1
Build
Three 200L columns: sand, biofilm-sand, membrane control.
STEP 2
Seed
Biofilm cultured 21 days on local seawater inoculum.
STEP 3
Run
112 days at 35 / 40 / 45 ppt, weekly particle counts.
STEP 4
Measure
FTIR-verified counts in 4 size bands, triplicate samples.
Notes: Flowchart beats bullets for methods. Mention triplication and FTIR verification unprompted.

## Slide 6
RESULTS
DEPT. OF ENVIRONMENTAL ENGINEERING
06
Biofilm-sand removed 93% — near membrane performance
Chart: 
| Sand only | Biofilm-sand | Membrane
Removal % (<300µm) | 41 | 93 | 97
KEY INSIGHT
Biofilm-sand reaches 93% removal vs 97% for membrane — at roughly one-fifth of the operating cost. The 4-point gap is the price of affordability.
Notes: Answer RQ1 explicitly: yes, above the 90% threshold at all salinities tested.

## Slide 7
DEPT. OF ENVIRONMENTAL ENGINEERING
07
$0.04/m³
Operating cost of the biofilm-sand design
vs $0.21/m³ membrane benchmark — inside the RQ3 target
Notes: STAR moment. Let it breathe 3 seconds, then answer RQ3.

## Slide 8
DISCUSSION
DEPT. OF ENVIRONMENTAL ENGINEERING
08
Salinity slowed start-up, not steady performance
45 ppt delayed biofilm maturity 9 days
Steady-state removal equalized after day 40 at all salinities.
Backwash cycle is the main OPEX driver
Optimizing backwash timing is the clearest cost lever.
Limitation: single polymer mix tested
Polyester fibers dominated; tire-wear particles untested.
40d
Days to steady state at the highest salinity.
Notes: Name limitations before the panel does — credibility. Backup slide has salinity curves.

## Slide 9
DEPT. OF ENVIRONMENTAL ENGINEERING
09
Affordable removal is achievable
Recommendation: pilot at plant scale (10 m³/day) with backwash optimization as phase two.
References and full datasets in appendix · Thank you — I welcome your questions
Notes: End on the so-what. Keep this slide up during Q&A; backup data slides follow.